## Slide 1: INTERFACING ARDUINO WITH THE BEAGLEBONE BLACK
SUBMITTED BY : AMANDEEP SINGH
STUDENT ID :C0761298
GROUP :2

## Slide 2: TABLE OF CONTENT
PROJECT OVERVIEW
REQUIREMENTS FOR INTERFACING
  Hardware Requirements
  Software Requirements
BRIEF INTRODUCTION OF BEAGLEBONE
  Pin Layout
INTRODUCTION TO ARDUINO MEGA
  Features
  Pin layout
INTERFACING OF ARDUINO MEGA
  Schematic layout
  Connections of Arduino mega and beaglebone black
  Enabling UART ports
  Libraries include in coding
  Coding
TERMINAL OUTPUT
REFERENCES

## Slide 3
PROJECT OVERVIEW

## Slide 4: RECAP
After the successful interfacing of buzzer, Servo motor, Vibration sensor, and Fingerprint sensor, the next task is interfacing of Arduino mega with beaglebone black.
GPIO communications is used for interfacing of buzzer, Servo motor, Vibration sensor except the fingerprint sensor in which UART was used.
For interfacing of Arduino mega with beaglebone black UART communication protocol is used.

## Slide 5: REQUIREMENTS
For interfacing of Arduino mega with beaglebone black there are various hardware and software requirements.

## Slide 6: HARDWARE REQUIREMENTS
Arduino mega
Beaglebone Black
Jumper Wires
USB cables to connect beaglebone and Arduino to the host machine.

## Slide 7: Software requirements
Arduino IDE
Ubuntu Terminal
GCC Compiler
GNU nano text editor

## Slide 8: BRIEF INTRODUCTION TO THE BEAGLEBONE BLACK

## Slide 9: PIN DISCRIPTION
These are the pins that are used for interfacing.

## Slide 10: ARDUINO MEGA
Used as a salve device in the project.
Known for its capabilities in handling more complex projects, the Arduino Mega 2560 gives your projects plenty of room and opportunities. It’s recommended for 3D printers and robotics projects with its 54 digital I/O pins, 16 analog inputs, and a large space.
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 11: Arduino Mega

## Slide 12: INTERFACING OF ARDUINO MEGA WITH BEAGLEBONE BLACK
Arduino mega is connected to the beaglebone using UART communication protocol.
BEAGLEBONE | ARDUINO
P9 11 | 19 RX1
P9 13 | 18 TX1
GND | GND

## Slide 13: COMMUNICATION PROTOCOL
Beaglebone and Arduino are communicating with each other by UART communication.
By definition, UART is a hardware communication protocol that uses asynchronous serial communication with configurable speed. Asynchronous means there is no clock signal to synchronize the output bits from the transmitting device going to the receiving end.

## Slide 14: UART COMMUNICATION
Arduino Mega has 4 UART Ports available, and we are using SERIAL 1 to perform the communication.
The Serial port 1 has pin 18- TX and Pin 19- RX.
These pins are connected to the Arduino to make the UART communication possible.

## Slide 15: SCHEMATIC DIAGRAM

## Slide 16: INTERFACING OF ARDUINO MEGA WITH BEAGLEBONE BLACK

## Slide 17: ENABLING THE UART PORT 4 OF BEAGLEBONE BLACK
We need to follow few steps to accomplish this task.
Make a file under the name setTty.sh.
Command used at the terminal is :
nano /usr/local/sbin/setTty.sh
In this file bash script is written to configure the ports on the beaglebone side.

## Slide 18: ENABLING THE UART PORT
After saving the file next step is to make this file executable that can be done by the following command on the terminal.
chmod 755 /usr/local/sbin/setTty.sh

## Slide 19: ENABLING THE UART PORT 4 OF BEAGLEBONE BLACK
Create a new file with the name testTty.sh.
Open the text editor with the sudo nano command.
nano /usr/local/sbin/testTty.sh.
Similarly make this file also executable like the last one.
chmod 755 /usr/local/sbin/testTty.sh.

## Slide 20: ENABLING THE UART PORT 4 OF BEAGLEBONE BLACK

## Slide 21: ENABLING THE UART PORT 4 OF BEAGLEBONE BLACK
Create the service configuration file that makes the system run it on startup
Command used : nano /lib/systemd/system/setTty.service.

## Slide 22: LIBRARIES INCLUDED
stdio.h
  Standard C input Output Library.
unistd.h
  defines miscellaneous symbolic constants and types, and declares miscellaneous functions.
string.h
  C Library for various String Operations.
termios.h
  Contains the definitions used by the terminal I/O interfaces.
fcntl.h // FIle control, Open, close.
time.h The Time library provides the data structures and functions required to retrieve the system time, perform time calculations, and output formatted strings that allow the time to be displayed in a variety of common formats.

## Slide 23: LIBRARIES INCLUDED
fcntl.h
  FIle control, Open, close.
time.h
  The Time library provides the data structures and functions required to retrieve the system time, perform time calculations, and output formatted strings that allow the time to be displayed in a variety of common formats.

## Slide 24: CODE FOR ARDUINO

## Slide 25: TERMINAL COMMANDS
Enter the command “ssh debian@192.168.7.2” here ssh command instruct the system to establish an encrypted secure connection with the host machine. Debian here represent the user_name that is being accessed on the host and then it is followed by an IP address.
Before continue to next step, the password “temppwd” must be entered.
ENTER PASSWORD HERE

## Slide 26: TERMINAL COMMANDS
Enter “ls” to list the files.
To compile and execute the code, enter the command “gcc Arduino_Interface.c -o Arduino.” Here Arduino_Interface.c is the program_name and Arduino is the executable file name. Afterwards, press Enter and write the Executable_name : “sudo ./ Arduino.”
Again, enter the password: temppwd
For compilation and execution

## Slide 27: CODING OF ARDUINO INTERFACING

## Slide 28: CODING OF ARDUINO INTERFACING

## Slide 29: TERMINAL OUTPUT

## Slide 30: TERMINAL OUTPUT

## Slide 31: REFERENCES
https://electronics.trev.id.au/2018/02/09/get-uart-serial-ports-working-beaglebone-black.
https://stackoverflow.com/questions/6947413/how-to-open-read-and-write-from-serial-port-in-c.
https://www.wikitechy.com/tutorials/linux/how-to-open-read-and-write-from-serial-port-in-c.
Tutorial - Running the Arduino IDE on the BeagleBone Black (onlogic.com)
https://www.youtube.com/watch?v=LubYc87S9tQ&ab_channel=BINARYUPDATES