## Slide 1: INTERFACING OF BUZZER WITH BEAGLEBONE BLACK
KIRANPREET KAUR GILL
GROUP #2

## Slide 2: CONTENT
PROJECT OVERVIEW
REQUIREMENTS FOR INTERFACING
  Hardware Requirements
  Software Requirements
INTRODUCTION TO BEAGLEBONE
  Pin Layout
  Features
INTRODUCTION TO BUZZER
  Types of Buzzer
  Features
INTERFACING OF BUZZER
  Schematic layout
  Connections of buzzer and beaglebone black
  Installing iobb library
  Coding of buzzer
TERMINAL OUTPUT
REFERENCES

## Slide 3: PROJECT OVERVIEW: IOT BASED BANK LOCKER SECURITY

## Slide 4: PROJECT OVERVIEW
The main objective of this project is to effectively control and manage the bank locker security using fingerprint sensor, passcode and camera.
The IOT based Bank locker security system uses an automated Safety vault with layered defense mechanism.

## Slide 5: REQUIREMENTS
For the completion of this project, the first task is the interfacing of buzzer with beaglebone black.
For buzzer interfacing, there are some hardware and software requirements.

## Slide 6: HARDWARE REQUIREMENTS
Beaglebone black
Buzzer
Jumper wires
USB Cable

## Slide 7: SOFTWARE REQUIREMENTS
Terminal
GCC compiler
GNU Nano editor

## Slide 8: INTRODUCTION TO BEAGLEBONE BLACK
Beaglebone Black is our main microcontroller unit as all the components are connected directly
It is a low-cost, community-supported development platform.

## Slide 9: PIN LAYOUT OF BEAGLEBONE BLACK

## Slide 10: FEATURES OF BEAGLEBONE BLACK
It has a range of IO including USB, SPI, I2C, UART, LCD, and GPIOs.
Connectivity
  USB client for power & communications
  USB host
  Ethernet
  HDMI
  2x 46 pin headers
Software Compatibility
  Debian
  Android
  Ubuntu
  Cloud9 IDE on Node.js w/ BoneScript library

## Slide 11: INTRODUCTION TO BUZZER
A buzzer or beeper is an audio signalling device, which may be mechanical, electromechanial, or piezoelectric (piezo for short). Typical uses of buzzers and beepers include alarm devices, timers, and confirmation of user input such as a mouse click or keystroke.

## Slide 12: TYPES OF BUZZER
Buzzers come in a variety of construction, size, and specifications. Different types and sizes of buzzers are used for different applications. Based on construction, there are the following kinds of buzzers:
Piezoelectric buzzers
Magnetic buzzers
Electromagnetic buzzers
Mechanical buzzers
Electromechanical buzzers

## Slide 13: FEATURES OF BUZZER
In this project, Mechanical buzzer is used with the following features:
Rated Voltage: 5V-12VDC
75dB a loud sound for alarm
Active drive inside buzzer and simplify your design, only needs to control buzzer on or off
Widely used in security and home alarm system, or other areas needs sound alarm

## Slide 14: FUNCTION OF BUZZER
The buzzer will start if anything abnormal like vibration, multiple wrong passwords and fingerprint mismatched etc. are detected

## Slide 15: INTERFACING OF BUZZER TO BEAGLEBONE BLACK
Buzzer is directly connected to the beaglebone black with the help of GPIO pins.
Function of buzzer is to make sound when something wrong happens.
BUZZER | PINS OF BEAGLEBONE BLACK
RED | P8.12
BLACK | P8.2

## Slide 16: SCHEMATIC DIAGRAM

## Slide 17: CONNECTION OF BUZZER AND BEAGLEBONE BLACK

## Slide 18: INSTALLING iobb LIBRARY
STEP1 : To install the library, initially use the command “ls” to get the list of file. Then, enter the command “cd iobb.” Here, it is used to go to the directory iobb and to open the library folder.

## Slide 19: INSTALLING iobb LIBRARY
STEP 2 : “Make” command is entered to next make executable file, then it require some time to execute the command and open the file.

## Slide 20: INSTALLING iobb LIBRARY
STEP 3: To install the make file “sudo make install” command is entered. Finally, the library is installed in the Beaglebone Black and is ready to use.

## Slide 21: CODING OF BUZZER

## Slide 22: TERMINAL COMMANDS
STEP 1: Enter the command “ssh debian@192.168.7.2” here ssh command instruct the system to establish an encrypted secure connection with the host machine. Debian here represent the user_name that is being accessed on the host and then it is followed by an IP address.

## Slide 23: TERMINAL COMMANDS
STEP2: Before continue to next step, the password “temppwd” must be entered.
Enter the password here.

## Slide 24: TERMINAL COMMANDS
STEP 3: Enter the command “sudo nano buzzerTest.c” to open Nano text editor and to directly write, edit and navigate the code and to get immediate onscreen feedback. Here, buzzerTest.c is the file name. Then enter the same password “temppwd.”
Here CTRL+O : save the code; then press enter; CTRL+X : to exit.
filename

## Slide 25: TERMINAL COMMANDS
STEP4: To compile and execute the code, enter the command “gcc buzzerTest.c -o buzzerTest liobb.” Here, buzzerTest.c is the program_name and buzzerTest is the executable file name. Afterwards, press Enter and write the Executable_name : “sudo ./buzzerTest.”
STEP5: Again enter the password: temppwd
Steps for Execution & Compilation

## Slide 26: TERMINAL OUTPUT

## Slide 27: BEEPING OF BUZZER

## Slide 28: REFERENCES
www.elinux.org/Beagleboard:BeagleBoneBlack
https://en.wikipedia.org/wiki/Buzzer#:~:text=History-,Electromechanical,which%20had%20a%20softer%20tone.
https://www.element14.com/community/community/designcenter/single-board-computers/next-genbeaglebone/blog/2013/10/10/bbb--beaglebone-black-io-library-for-c
https://github.com/shabaz123/iobb/blob/master/BBBio_lib/BBBiolib.c
https://www.geeksforgeeks.org/gcc-command-in-linux-with-examples/#:~:text=GCC%20stands%20for%20GNU%20Compiler,C%20and%20Objective%20C%2B%2B.

## Slide 29: REFERENCES
https://linuxize.com/post/how-to-use-nano-text-editor/
https://maker.pro/linux/tutorial/basic-linux-commands-for-beginners
https://www.engineersgarage.com/tech-articles/buzzers-types-transducer-indicator-piezo-magnetic/
https://easyeda.com/editor#id=7cda8be44cda42db86c29f6dba7824a9
UHPPOTE Mechanical Buzzer Sounder 12VDC Continuous Beep with Leads 75dB for Access Control and Buzz-in System (Pack of 5) (qprographx.com)

## Slide 30: THANK YOU